# Text boxes

Explore engineering careers at www.tomorrowsengineers.org.uk

Ionising 
radiation

High frequency 
electromagnetic radiation with 
high energy, like x-rays and 
gamma rays, can remove electrons 
and turn atoms into ions. This is 
called ionizing radiation. Low 
energy electromagnetic 
radiation like visible light or 
radio waves can’t do this.

Ionising radiation

Is it good to hold a 
radiation source next to your brain?

How long do you use the phone 
for each day?

All cell phones give out electromagnetic radiation. As you hold the phone close 
to your head some people are concerned that this radiation may cause some 
sort of harm.

Microwaves are not like x-rays, they don’t have enough energy to strip 
electrons from atoms. Microwaves are non-ionising radiation. But radio 
waves and microwaves can cause heating or thermal changes in the body.

As it comes in contact with substances Radio Frequency (RF) energy may be 
reflected (like from metal), pass through with no energy loss (like with glass), 
or get absorbed (like with human tissue). This makes the temperature of the 
tissue go up.

It seems that the absorption of electromagnetic energy depends on its frequency:

- Frequencies higher than 10,000 MHz are absorbed in the outer skin.

- Frequencies between 10,000 MHz and 2,500 MHz penetrate more deeply 
(3 mm to 2 cm) and RF at 2,500 MHz to 1,300 MHz, can damage organs.

- Mobile phones use a range from 400 to 2,000 MHz.

How this RF radiation heats the body tissue depends on several factors. Heating will 
be worst in tissue with high water content, such as muscle. Less heating happens
in bone and fat. Heating will be related to the power of the RF radiation. 4 W/kg is a 
hazardous level. Standards setting organizations set maximum exposure levels at 
one tenth (10%) of this value. A mobile phone typically transmits 2 W of power.

But the debate doesn’t stop there. Some people have also blamed mobile phones for:

- Changes in blood chemistry

- Changes in behaviour

- Cancer tumours

- Slower reaction times

- Loss of attention, memory, concentration, dizziness, headaches, 
heart racing, and others.

So far nothing has been proved but the debate will continue.