## Slide 1
Simple Circuits

## Slide 2
We are going to make this circuit…
wire
battery
(in holder)
motor
switch

## Slide 3
You Will Need:
1 motor
1 battery pack
1 switch
3 lengths of wire

## Slide 4
Preparing the wires to make the circuit
Cut the wire to the length needed.
Using wire strippers, take off about 10 mm of plastic coating from the end.
Twist the exposed stands of wire to join them together.
wire
Stripped end of wire
Twist wire this way

## Slide 5
Joining two wires together
wire
wire
Twist the exposed wires together
Using wire strippers, take off about 10 mm of plastic coating from the end of each wire.
Twist the exposed stands of wire to join them together.
Wrap sticky tape around the joint.

## Slide 6
Making a switch from a paper clip
Push two metal fasteners through a piece of card.
Wrap a wire around the back of each metal fastener.
Slide a paper clip under one of the fasteners, on the top side.
If you move the paper clip round so it touches the other fastener, it completes the circuit.
wire
wire
stud
stud
paper clip

## Slide 7
The completed circuit…
wire
battery
(in holder)
motor
switch