| Design an automatic lighting system |
| --- |
| Use the BBC micro:bit programmable system to create a working prototype |
| Subjects: Design & Technology, Computing Approx. time: 60 - 120 minutes depending on ability and prior experience of learners |  | Key words / Topics BBC micro:bit system and sub-system input, process, output accelerometer sound output, buzzer programmable components embedded intelligence |
| Suggested Learning Outcomes |  |  |
| To understand a block systems diagram of the lighting system. To select an appropriate input device for the system. To successfully program the BBC micro:bit so that the system meets the design criteria. |
| Introduction |  |  |
| This is one of a series of resources to support the use of the BBC micro:bit in Design and Technology lessons. People are always looking for ways to save energy. It is estimated that the average UK homeowner could save up to £240 a year alone on the cost of lighting their home. In this unit of learning, learners will use the BBC micro:bit to develop a prototype for an LED based automatic home lighting system, designed to save energy. |
| Purpose of this activity In this activity, learners will develop their programmable lighting system using the BBC micro:bit. This could be used as a main lesson activity with ‘What am I? Inputs and outputs’ as a starter and ‘Resistor calculation’ as an extension activity. It is an ideal exercise for learners to develop programming skills, make use of programmable components and embed intelligence into a product design. |
| Activity |  | Teacher notes |
| 1. Design Brief Teacher to introduce the situation and design brief to learners. Use the teacher presentation as a guide for this. Emphasise that they will be using the BBC micro:bit system, which is a programmable system, to create their solution. Situation: People are always looking for ways to save energy. It is estimated that the average UK homeowner could save up to £240 a year alone on the cost of lighting their home. Brief: Using the BBC micro:bit, create a prototype for an automatic lighting system for the home. The system must be able to turn the lighting on when somebody enters a room. It must also turn the lighting off when people leave the room, or after a timed period to save energy. 2. Systems diagram Introduce the systems diagram for the automatic lighting system. Discuss this with learners. What do input, process and output mean? What are the key physical parts of the system and their functions? 3. Design criteria for the system Go through the design criteria with learners. Question them as to what each of the criteria might mean in practice in terms of producing their system. How might they meet each of the criteria? 4. Input device – motion sensor Selection of an appropriate motion sensing input device for the system. This should detect when someone enters the room so that the system knows when to turn the light on. This (or an additional sensor) should also be able to detect when people are no longer in the room. Use teacher PowerPoint slide to show what is available to learners (teacher should adapt this slide depending on what is available in their school). Possible sensor inputs: PIR sensor – passive infrared sensor. Often used in commercial home security and lighting systems. Measures infrared light radiating from objects in its field of view. Reed switch – magnetically operated switch. A magnet is placed on one side of a door and the switch on the other. When the door is opened the circuit is broken. LDR (light dependent resistor) – could be used in conjunction with another resistor to form a potential divider that can be used as either a light or dark sensor (dark when a door is closed, light when opened). Pressure pad – placed near the entry to the room. The circuit is ‘made’ when a person stands on top of it. 5. Output device A hi-bright LED can be used to produce the light for the lighting system prototype. Learners to use an appropriate method, such as crocodile clips, to attach the LED and sensor circuit to the appropriate ports of the BBC micro:bit. A protective resistor may also be needed for the LED. 6. Writing the program Learners begin writing their program to meet the design criteria using the example program as a guide where necessary. 7. Progress review Review learner progress part way through the activity and recap key points as necessary. Refer to the example program where appropriate to help guide learners. 8. Downloading program and testing Learners download and test their program, refining and improving it as necessary. |  | The IET TV video – Saving Lighting Energy https://tv.theiet.org/Index.html?videoid=7299 can be shown as an introduction or starter for activities in this unit of work. This activity can be attempted by learners as individuals, in pairs or in small groups. If learners have not seen or used a block systems diagram before it would be necessary to describe this in more detail (i.e. what is meant by input, process, output etc). Selecting and using external inputs/outputs When selecting inputs, learners could either be guided by the teacher using the teacher PowerPoint, or be given more free reign depending on ability and availability of components in school. When using an analogue sensor on a digital input pin this web link can be used as guidance on the circuit needed. For example, when using an LDR as part of a potential divider to create a light or dark sensor. Learners will need access to suitable methods of connecting the sensors and outputs to the BBC micro:bit. A simple way to do this is to use crocodile clips. Block connectors could also be used. Although more permanent hardwired methods could be used these should be avoided if the BBC micro:bit is to be reused with other learners or different classes. When using a hi-bright LED, a protective resistor may be needed. This should be connected between the anode leg of the LED and the output port being used on the BBC micro:bit. Teachers are advised to refer to the BBC micro:bit’s specification when selecting input and output devices to use with it. Programming the BBC micro:bit and example When writing the program, low ability learners or those who have not done programming before may benefit from writing, experimenting with and downloading the example program shown on the Teacher PowerPoint. They can use this as a base for their own program. This is provided as JavaScript Blocks Editor Powered by Microsoft MakeCode (microbit-lighting-jsb.hex) and Python Editor code (lighting.py). Teachers will need to decide which programming editor is the most suitable for their learners. This program assumes that an LED output has been attached to pin 1 of the BBC micro:bit. It also assumes that a digital input has been attached to pin 0. This program will turn on an output attached to pin 1 when a high input signal is received on pin 0. Learners will need to add a timing function to keep the output LED on for a set amount of time and/or a way of turning the lighting off when no longer needed. To open the example programs: Go to http://microbit.org/code/ Find the appropriate programming editor. Click on ‘Let’s Code’. Drag the relevant program file from the folder where it is stored to the work area on screen. Visit http://support.microbit.org/support/home for help and further support if needed. |
| Differentiation |  |  |
| Basic |  | Extension |
| Learners can write the example program directly into the programming software and download it as a starting point. They can then develop this further as required. The example program is included in the accompanying teacher PowerPoint. |  | Learners could develop more prototypes using additional BBC micro:bits (one for each lighting device). This could involve the use of different sensors – testing which works the best. They could also use 3D modelling software to design a possible housing for their lighting system. This should show the positioning of the sensors and LED outputs and describe the materials and processes that would need to be used to make it. |
| Resources |  | Required files |
| Projector/Whiteboard BBC micro:bit system and online programming software Internet (to access programming software) Hi-bright LEDs and protective resistors Suitable motion sensors Crocodile clips or other wiring options (to attach input and output devices) |  | Developing the Programmable System presentation Example BBC micro:bit JavaScript Blocks Editor and Python Editor programs (also provided as .hex and .py files). |
| Additional websites |  |  |
| The following websites can be used for additional technical information or to provide a wider context to the development of the system. IET TV – Saving Lighting Energy: Supporting IET TV video - ideal for use as part of a starter or introductory activity to support this resource. https://tv.theiet.org/Index.html?videoid=7299 BBC micro:bit website: Website containing everything needed to get started with using the BBC micro:bit! https://microbit.org/ Electronics Club – Other Components: Website containing technical information about a range of components that are used as input and output devices (scroll to the bottom of the page). http://electronicsclub.info/other.htm Wikipedia – PIR sensor: Page describing PIR sensors, what they are and how they work. https://en.wikipedia.org/wiki/Passive_infrared_sensor Instructables – LEDs and Resistors: Technical information on LEDs and protective resistors, including how to select the correct values. http://www.instructables.com/id/Choosing-The-Resistor-To-Use-With-LEDs GCSE Bitesize – Systems: Useful revision notes and video covering the basics of systems and the use of block diagrams. https://www.bbc.com/bitesize/guides/zh8ck2p/revision/1 Wikipedia – Sustainable Lighting: Information about sustainable lighting used in buildings. https://en.wikipedia.org/wiki/Sustainable_lighting |
| Related activities (to build a full lesson) |  |  |
| Starters ACTIVITY: What am I? Inputs and outputs IET TV VIDEO – Saving Lighting Energy https://tv.theiet.org/Index.html?videoid=7299 Main ACTIVITY: Design an automatic lighting system | Plenary ACTIVITY: Resistor calculation Opportunities within activity for presentations, peer/self assessment Reflection on Objectives and PLTS skills used |

The Engineering Context

Sustainable lighting is an ideal topic for teaching about programmable components and embedded intelligence in products. These are key parts of the 2014 programme of study for Design and Technology at key stage 3. It is also an ideal vehicle for using the BBC micro:bit in the classroom and developing the programming skills of learners.

| Curriculum links |
| --- |
| England: National Curriculum Design & Technology KS3 3c, 4c, 4d Computing KS3 Pupils should be taught to: design, use and evaluate computational abstractions that model the state and behaviour of real-world problems and physical systems undertake creative projects that involve selecting, using, and combining multiple applications, preferably across a range of devices, to achieve challenging goals, including collecting and analysing data and meeting the needs of known users | Northern Ireland: Curriculum Technology & Design KS3 Knowledge and Skills: Control – incorporate control systems, such as mechanical, electronic or computer-based, in products and understand how these can be employed to achieve desired effects. KS3 Objective 1: Respond to a personal design challenge in relation to their own lifestyle. Learning Outcomes: Show deeper understanding by thinking critically and flexibly, solving problems and making informed decisions, using Mathematics and ICT where appropriate. Demonstrate creativity and initiative when developing ideas and following them through. |
| Scotland: Curriculum for Excellence Technologies TCH 3-01a, TCH 3-03a, TCH 3-04a,TCH 3-13a | Wales: National Curriculum Design and Technology KS3 Skills: Designing 1 KS3 Skills: Systems and Controls 16, 18, 20, 21 |
| GCSE D&T AQA D&T 3.1.4, 3.3.4, 3.3.7 Edexcel D&T 1.6, 1.7, 1.16.1c, 1.6, 1.7, 1.16.1c, 5.1.1, 5.2.1, 5.2.2, 5.2.3 Eduqas D&T 2.1 Core: 5, 6 2.1 Systems: 1, 2 OCR D&T 4.2a ii, 5.2b, 6.4 | GCSE Engineering AQA Engineering 3.3.2, 3.3.3, 3.4.2 |

Assessment opportunities

Regular questioning throughout the activity, review of progress at key intervals and formal assessment of the finished program and the working system.

Personal, learning & thinking skills (PLTS)

Creative thinker Independent enquirer Team worker (if done as a team activity) Self manager Effective participator