## Slide 1
Building a Simple Electric Motor

## Slide 2
Step 1: Wind the Field Coil
Cut about 800-900 mm of varnished copper wire.
Wind this around the black plastic tube 10 times, then push it off the tube.
axle
axle
30 mm
30 mm
From each end, wind the wire around the loop to hold it together.
Straighten the ends to form two axles.
Trim each axle so that it is about 30 mm long.

## Slide 3
Step 2: Make the Two End Contacts
Cut about 150 mm of the tinned copper wire and make the shape shown.
Repeat this step, as you will need two of these end contacts.
60 mm
Hint: the shape can be made by wrapping the wire around the shaft of a small screwdriver.

## Slide 4
Step 3: Attach the End Contacts to the Battery
Wrap the elastic band around the battery. You may need to ‘double up’ the band so it holds tight.
Elastic band
magnet
Attach the end contacts as shown.
Clip the magnet to the case.
Using ‘blu-tack’, support the assembly on a work bench so that it is standing up.

## Slide 5
Step 4: Prepare the Field Coil
Use wet and dry paper to remove the varnish from one side of the axle at each end.
Hints:
This part is quite tricky, so take your time.
Be careful not to remove all of the varnish.
Place paper under the axle so you don’t damage the table top.
axle
Plane of coil
Remove varnish here only

## Slide 6
Step 5: Assemble the motor
Place the field coil so that its ends go through the loops on the end contacts.
Congratulations, your motor is complete. With a little push, it should spin rapidly under its own power!

## Slide 7
What if it doesn’t work?
Check that both end contacts are firmly touching the metal ends of the battery.
Check that the battery still has charge.
Check that you have only removed the varnish from one side of the wire on the axle.
If all these don’t work – ask for help!

## Slide 8
Experimental Investigations
Which direction does your motor spin? Investigate how you can make it spin in the opposite direction.
Place a radio near the motor, set to ‘medium wave’/MW. Why does the radio crackle? What happens if the radio is set to FM instead?
Make another coil, removing varnish from the whole of the axis at each end. Investigate how this changes the behaviour of the motor.