## Slide 1
Wonderful Weaving
Using wool to make a woven product

## Slide 2: Equipment
Cardboard
Wool
Large eye blunt needle
Masking tape
Notes: Recycling – using cardboard from postal packaging, paper boxes etc
A5 sized piece approx. 15 x 21cm – larger sizes can be used for complexity or ease of use.
*also need masking tape to secure Warp threads*
Instead of using new wool, can use fabric strips, ribbons or other suitable materials.

## Slide 3: Step 1
Measure and mark out slits for warp threads on the shortest edges of cardboard, 1 cm apart
Cut slits 1 cm deep
Notes: Ensure there are an EVEN number of warp strings.
Warp threads can be spaced up to 1.5 cm to help with dexterity of required.

## Slide 4: Step 2
Wrap the wool around alternate slits
Stick the ends with masking tape
Notes: Use alternating colours for the Warp threads – aids with under and over.
Numbering the warp strings can help, 1212

## Slide 5: Step 3
Thread blunt needle with wool
Leave tail when begin weaving
‘Under and Over’
Notes: If using numbered warp threads, remind them ‘12121212’
Extension: design a pattern that can be woven in, for example equal sized stripes or a shape.

## Slide 6: Step 4
Change colour when wool runs out
Leave tail when changing colour
Notes: Try and get all tails on the same side, makes the neatening process easier at the end.

## Slide 7: Step 5
Continue weaving until approximately 3 cm from the bottom
Notes: Check the tension of the weaving, otherwise the material with narrow as in the above example.

## Slide 8: Step 6
Thread the tails into the looped ends of the weft

## Slide 9: Step 7
The weaving is complete!
Notes: The weaving is now complete.
This can be displayed on the loom or be cut from the loom and used as a wall hanging.
Continue with Step 8 if removing from the loom.

## Slide 10: Step 8
Turn the card over and remove tape
Cut warp across the middle
Notes: The weaving is now complete.
This can be displayed on the loom or be cut from the loom and used as a wall hanging.

## Slide 11: Step 9
Turn the loom over to the front
Pull 2 adjacent warp threads from the slits and knot together
Repeat with each pair of warp yarns
Notes: The weaving is now complete.
This can be displayed on the loom or be cut from the loom and used as a wall hanging.

## Slide 12: Step 10
Remove the weave from the loom
Notes: The weaving is now complete.
This can be displayed on the loom or be cut from the loom and used as a wall hanging.

## Slide 13: Step 11
Weaving can be displayed as a wall hanging
Use loom to create display point
Notes: The weaving is now complete.
This can be displayed on the loom or be cut from the loom and used as a wall hanging.

## Slide 14
Notes: The weaving is now complete.
This can be displayed on the loom or be cut from the loom and used as a wall hanging.