| Four experiments with magnets |
| --- |
| Four fun experiments using powerful magnets |
| Subject(s): Science, Design & Technology, Engineering Approx time: 60 mins |  | Key words / Topics: electromagnetism electromagnetic induction chaos theory magnetic fields applications & implications of science |
| Suggested Learning Outcomes |  |  |
| Understand practical applications of magnets and magnetism Understand how electromagnetic induction works Understand the scientific principle of ‘chaos’ Understand how magnetic fields penetrate the human body. |
| Introduction |  |  |
| This activity sheet was developed with the support and participation of the School of Engineering at Cardiff University (www.engineering.cardiff.ac.uk). Magnets are objects that produce a magnetic field that can either attract or repel other magnetic materials. This has many potential uses, such as in power generation, speaker design and advanced transport systems, such as MAGLEV trains. This is a series of practical experiments that demonstrate various different scientific principles related to magnets and magnetism. Purpose of this activity These activities provide a quick, engaging set of tasks designed to demonstrate various theories related to the use of magnets, such as electromagnetic induction, chaos theory and magnetic fields. Although mainly designed as science activities, they could also be used as an introduction to power generation or the potential uses of magnets in Design and Technology and Engineering projects. |
| Activity |  | Teacher notes |
| Introduction to magnet kit and safety Introduce the kit to be used in the experiments and the health and safety rules to be followed when using magnets (the resources section of this document contains the details of the items of kit needed). Learners should follow the following set of instructions to successfully conduct each experiment: Experiment 1: Dropping magnets down a tube Conduct a ‘free-fall’ test. Drop the magnets through a height of around 20 cm. Try to measure the time taken for the magnets to fall. Drop the magnets down the plastic tube. Describe the differences observed compared to the ‘free-fall’ test. Try to measure the time taken for the magnets to fall through the plastic tube. Drop the magnets down the copper tube. Measure the time taken for the magnets to fall through the copper tube. Describe what happens and explain your observations. In your explanation try to answer the following questions: What determines the speed at which the magnet falls? Why is the underlying scientific principle in action here so important for our everyday lives? Experiment 2: The chaotic pendulum Carefully separate the two magnets by sliding them apart. Fix the magnets to a flat surface using blu-tack. They should be placed approximately 6 cm apart. Make a pendulum using a steel nut as the pendulum’s “bob” (the bit that swings), tied to a 50 cm long piece of cotton thread supported vertically above the pair of magnets. Adjust the length of string so that the bob swings about 1 cm above the floor level at its lowest point. Observe and describe the motion of the pendulum. Eventually it should come to rest near one of the magnets. Can you predict which one, based upon the position from which the pendulum started swinging? Experiment 3: “Aaarrgghh!!! Spider!” The two magnets are so powerful that their magnetic fields are still quite large even a few cm away from them. To demonstrate this, place one of the magnets in the palm of your upturned hand and then move the other magnet underneath your hand. You should find that the magnet in your palm moves, as it is attracted to (or repelled by) the magnet underneath. Place an inanimate object, such as a plastic spider, onto one of the magnets. Try to make it move as if it is alive! |  | The supporting PowerPoint contains instructions for completing the experiments. This can be shared with learners via a projector/interactive whiteboard. Experiment 1 This experiment demonstrates the principle of electromagnetic induction, which is the conventional way of generating electricity. When dropped down the copper tube, the falling magnet induces an eddy current around the tube wall that produces an upwards force on it. This exactly balances gravity, causing it to fall with constant velocity (by Newton’s first law of motion). The time taken for it to fall through the tube is proportional to the electrical conductivity of the tube wall. This can be tested by dropping the magnet down tubes of the same size but made of different metals. Copper is second only to silver in having the highest conductivity at room temperature. The plastic tube cannot support an electrical current, allowing the magnet to accelerate under gravity in the usual way. Simple calculations show that it should take 0.2 s to free-fall by 20 cm - too fast to measure easily. A longer piece of straight copper pipe than that suggested can be cheaply obtained from most hardware stores. A piece that is at least 1 m in length will give an even more impressive experimental result. Experiment 2 This demonstrates the general principle of ‘chaos’. That is the chaotic (i.e. apparently random) motion of the pendulum before it finally settles down. Starting the pendulum swinging near one magnet is no guarantee that it will settle next to this magnet. You could further explain how chaos has huge consequences for our physical world. The initial separation the magnets (step 1) is best done by sliding, rather than pulling them apart. When supporting the magnets vertically (step 2) a chair works well for this purpose. Experiment 3 This demonstrates that magnetic fields penetrate the human body and are harmless. An example, such as medical imaging machines (e.g. MRI scanners), could be shared with learners for context. These use very large magnetic fields to affect the spins of the nuclei of the atoms present within the body, allowing images of internal organs to be produced. This could also be compared this with the harmful alternative of using X-rays. Step 3 works well when moving such objects around on table tops, using a magnet below. Suggested lesson format These experiments can be completed individually by students, or in small groups. They could be delivered as single integrated lesson spilt into three parts: Part A - Newtonian Interaction Part B - Coulomb Interaction Part C - combined/unifying approach Health and safety It is very important that health and safety rules are followed when working with magnets. The suggested magnets for this activity are made from an alloy of the rare earth metal neodymium (Nd), which is used to make some of the strongest permanent magnets. When using them with students, the following should be implemented: Keep them away from heart pacemakers Ensure students do not attempt to swallow them Explain to students that they are brittle and can shatter into very sharp bits if allowed to fly together Keep them away from credit cards, iPods, mobile phones and TVs |
| Differentiation |  |  |
| Basic |  | Extension |
| Organise as group activities with higher ability leaners supporting lower ability learners. Use sentence starters and prompts to assist learners with describing, explaining and discussing the results of each experiment. Use a technician to pre-assemble the pendulum for experiment 2. |  | Discuss current and potential future engineering applications of electromagnetic induction. Research the consequences of ‘chaos theory’ in the physical world. Investigate and explain the applications and advantages of using magnetic fields in healthcare. |
| Resources |  | Required files |
| Projector/Whiteboard Magnet kit 2 neodymium magnets - 12mm diameter x 2mm thick e.g. F312-20 from www.first4magnets.com 1 off 15mm diameter x 200mm length plastic radiator pipe sleeves e.g. 0000004002178 from B&Q DIY www.diy.com 1 off 15mm diameter x 200mm length copper plumbing pipe (cut to 200mm length plus deburred internal openings) e.g. 5034579002276 from B&Q DIY www.diy.com Cost to make 10 kits from above supplies: Magnets £10 Plastic pipes £10 Copper pipes £10 Total cost is approximately £30 (or £3 per kit) Additional resources Sticky tape, blu-tack, steel nut, cotton thread and chairs |  | Four experiments with magnets (Presentation) |
| Additional websites |  |  |
| GCSE Bitesize: Introduction to magnets and their properties. https://www.bbc.co.uk/education/guides/zxxbkqt/revision Howstuffworks: How MAGLEV trains work https://science.howstuffworks.com/transport/engines-equipment/maglev-train.htm GCSE Bitesize: How electromagnetic induction is used to create electricity. https://www.bbc.co.uk/bitesize/guides/zqys97h/revision/1 Wikipedia: An introduction to ‘chaos theory’. https://en.wikipedia.org/wiki/Chaos_theory |
| Related activities (to build a full lesson) |  |  |
| Starters (Options) Research the basic properties of magnets Main (Options) ACTIVITY: Magnet Madness ACTIVITY: Motor Madness ACTIVITY: Overcoming friction | Plenary Opportunities within activity for presentations and peer/self-assessment of experiment outcomes Reflection on Objectives and PLT skills used Investigate practical uses of the theories explored |

The Engineering Context

Applications of magnets and magnetism

| Curriculum links |
| --- |
| England: National Curriculum Science KS3 2a, 2b, 2c, 2d, 2e, 27h, 37a, 37a, 37d KS4 Magnetism and electromagnetism Design & Technology KS3 1a, 3a, 3b, 4a GCSE AQA Engineering 3.1.3, 3.3.2 AQA Design and Technology 3.1.1, 3.1.2 Edexcel Design and Technology 1.2.2b, c, 1.3.2 Eduqas Design and Technology 2.1 Core: 3 2.2 Core: 2 OCR Design and Technology 1.1a i, 3.2 AQA Physics 4.5.1.2, 4.7.1, 4.7.2 Edexcel Physics 9.1a, 12.1, 12.2, 12.3, 12.4, 12.7, 12.11, 13.1P, 13.2, 13.3P Eduqas Physics 3.1a, 8.1a, 8.1b, 8.2e OCR Gateway Science Physics A P2.2a, P4.1a, P4.1e, P4.2a, P4.2d OCR Twenty First Century Science Physics B P2.1.1, P2.2.3, P3.5.1, P3.5.2, P3.6.1, P3.6.4, P3.7.1, P4.1.3 AQA Combined Science: Synergy 4.6.1.1, 4.6.3 AQA Combined Science: Trilogy 6.5.1.2, 6.7.1, 6.7.2 Edexcel Combined Science 9.1a, 12.1, 12.2, 12.3, 12.4, 12.7,12.11, 13.2 Eduqas Combined Science 3a, 8.1a, 8.1b, 8.2e OCR Gateway Science Combined Science A P2.2a, P3.3a, P3.3c, P3.3h, P3.3k OCR Twenty First Century Science Combined Science B P2.1.1, P2.2.3, P3.4.1, P3.4.2, P4.1.2 | Northern Ireland Curriculum Science Developing pupils’ Knowledge, Understanding and Skills develop skills in scientific methods of enquiry to further scientific knowledge and understanding: planning for investigations, obtaining evidence, presenting and interpreting results; Learn about forces and energy Technology & Design (Objective 2) Developing pupils as Contributors to Society Explore technical inventions and designs that have met a social need cost-effectively |
|  | Scotland: Curriculum for Excellence Sciences SCN 4-08a 4-20a Technologies TCH 3-01a |
|  | Wales: National Curriculum Design and Technology KS3 Skills (Designing 2) KS3 Range (Systems and controls 16) Science KS3 Skills (Enquiry 1, 2) KS3 Range (How things work 3) |

Assessment opportunities

Assess learner responses when describing and explaining the results of each experiment. Provide verbal feedback to guide learning during the activities. Self and peer assessment of experiment outcomes.

Personal, learning & thinking skills (PLTS)

Independent Enquirers Effective Participants Team Workers