## Slide 1
Make a doorbell circuit

## Slide 2
We are going to make this circuit…
wire
battery
(in holder)
buzzer
switch

## Slide 3
wire
battery
(in holder)
switch
You Will Need:
1 motor
1 battery holder
1 switch
3 lengths of wire
buzzer

## Slide 4
Preparing the wires to make the circuit
Cut the wire to the length needed.
Using wire strippers, take off about 10 mm of plastic coating from the end.
Twist the exposed stands of wire to join them together.
wire
Stripped end of wire
Twist wire this way

## Slide 5
Joining two wires together
wire
wire
Twist the exposed wires together
Using wire strippers, take off about 10 mm of plastic coating from the end of each wire.
Twist the exposed stands of wire to join them together.
Wrap sticky tape around the joint.

## Slide 6
Making a switch from two metal fasteners
Fold the card across the middle.
Push two metal fasteners through the card, one each side of the fold.
Wrap a wire around the back of each metal fastener.
If you fold the card so the two studs touch, it completes the circuit.
wire
wire
stud
stud

## Slide 7
The finished circuit…
wire
battery
(in holder)
buzzer
switch